## Slide 1: Host to Host Layer

## Slide 2: Protocols on the Host to Host Layer
Transmission Control Protocol: Takes large blocks of information from an application and breaks them into segments. It numbers and sequences each segment so that the destination’s TCP stack can put into the order the application intended.
TCP contacts the destination TCP to establish a connection
  Known as connection oriented
TCP is a full duplex, connection oriented, reliable and accurate protocol, but establishing all these terms and conditions, in addition to error checking
  Something so perfect comes with consequences NETWORK OVERHEAD

## Slide 3: Protocols on the Host to Host Layer
UDP: Is basically the scaled down economy model of TCP, which is why UDP is sometimes referred to as a thin protocol.
UDP does not offer all bells and whistle that TCP does
  No sequencing
  No virtual circuit (connection-less oriented)
This can result is some garbled data

## Slide 4: Protocols on the Host to Host Layer
TCP | UDP
Sequenced | Unsequenced
Reliable | Unreliable
Connection-oriented | Connectionless
Virtual Circuit | Low Overhead
Acknowledgements | No Acknowledgments
Windowing flow control | No windowing or flow control of any type

## Slide 5: Protocols on the Host to Host Layer
TCP | UDP
telnet 23 | SNMP 161
SMTP 25 | TFTP 69
HTTP 80 | DNS 53
FTP 20, 21 | BooTPS/DHCP 67
HTTPS 443 | 
SSH 22 | 
POP 110 | 
NTP 123 | 
IMAP4 143 | 
PORT NUMBERS FOR BOTH PROTOCOLS