## Slide 1: Internet Layer Protocol and Network Access

## Slide 2: The IP protocol
There are two main reasons for internet layer’s existence
  Routing
  Providing a single network interface of the upper layers
Without this layer, application programmers would need to write “hooks” into every one of their applications for each different Network Access Protocol.
IP provides on single network interface for the upper layer protocols.
List of important protocols at the internet layer
  IP
  ICMP
  ARP

## Slide 3: IP Protocol
For now, understand that IP looks at each packet’s address. Then using a routing table, it decides where a packet is to be sent next, choosing the best path to send it upon.
IP receives segments from the Host to Host layer and fragments them into datagrams if necessary. IP then reassembles datagrams back into segments on the receiving side.
Each datagram is assigned the IP address of the sender and that of the recipient.
Routing decisions based on packets destination IP addresses

## Slide 4: Protocols and Protocols Numbers for IP
Protocol | Protocol Number
ICMP | 1
IP in IP (TUNNELING) | 4
TCP | 6
UDP | 17
EIGRP | 88
OSPF | 89
IPv6 | 41
GRE | 47
Layer 2 tunnel (L2TP) | 115