## Slide 1: Network Address Range

## Slide 2: Network Addressing
An IP address, which is a logical address, is separated into two parts:
  The Network Address
  The Host Address
The network address will uniquely identify the network your node resides in.
The host address will identify the node that belongs to the network
All this is possible because of the subnet mask
  255.255.255.0

## Slide 3: Class A Range
The powers that be made the range of a class A the following:
  0XXXXXXX = 0
  01111111 = 127
So by their definition the range of a class A is from 0 – 127
But this does not take into consideration IP addresses that are reserved.
Will discuss this later

## Slide 4: Class B Range
The powers that be made the range of a class B the following:
  10000000 = 128
  10111111 = 191
So by their definition the range of a class B is from 128 – 191
Will dive deeper into this later

## Slide 5: Class C Range
The powers that be made the range of a class C the following:
  11000000 = 128
  11011111 = 191
So by their definition the range of a class C is from 192 – 223
Will dive deeper into this later

## Slide 6: Network Addresses D & E
The D range is for Multicast purposes: 224 – 239
The E range is for Scientific purposes: 240 -255
But once again I will discuss a little bit more later