## Slide 1: Classes of Addresses

## Slide 2: Class A address range
Previous lecture we were told that the Network range for a class A address was 0000000 – 01111111
But we need to know the actual range we can uses and what octet are we looking at:
  To classify an address you look at the first octet
  For a class A address
    1 – 126
    This is the actual usable range, within the first octet
Example: 1.2.3.4, 50.200.201.201 or 126.255.255.254

## Slide 3: Class B address range
Previous lecture we were told that the Network range for a class B address was 10000000 – 10111111
But we need to know the actual range we can uses and what octet are we looking at:
  To classify an address you look at the first octet
  For a class B address
    128 - 191
    This is the actual usable range, within the first octet
Example: 130.15.8.200, 168.192.181 or 191.255.255.254

## Slide 4: Class C address range
Previous lecture we were told that the Network range for a class C address was 11000000 – 11011111
But we need to know the actual range we can uses and what octet are we looking at:
  To classify an address you look at the first octet
  For a class C address
    192 - 223
    This is the actual usable range, within the first octet
Example: 192.15.10.95, 200.201.202.203 OR 223.255.255.254

## Slide 5: Class D and E Range
Class D range is for multicast: 224 – 239
  This is the actual usable range
  Routers use multicast address to send updates
    RIP 224.0.0.9
    EIGRP 224.0.0.10
    OSPF 224.0.0.5 and 224.0.0.6
Class E Range
  Is a black ops range
  240 – 255
  Not used in actual networks